Judge Ito's Clearance Specs www.jrsrotaryperformance.com
I hope this helps everybody out a little. These specs have proven reliability and performance. For my Naturally Aspirated engines I like a very tight fit with every single seal. Since N/A engines depend so much on compression and vacuum to make power, I pay close attention to a tight fit.
For Turbo, Supercharged and Nitrous engines I have different clearances. When I clearance an engine with a power adder like Turbo or Nitrous I keep in-mind that this engine is getting artificially increased compression or twice as much more oxygen in comparison to N/A engines. In return I clearance with a bit more GAP then N/A engines. I try to allow more of a leak down from the clearance for turbo charged engines then N/A. With this leak down (from a slightly bigger GAP) for turbo and nitrous engines, I have found some reliability. Imagine if the engine does not have somewhere to leak some compression from a 35lbs boost engine, with out this slightly bigger GAP, the engine is under some serious pressure on Apex Seals, Corner Seals and Side Seals and the possibility for broken seals are present. 

With this explanation I'll give away some of my specs that have worked incredible for me.
1) N/A engines.
I clearance my Apex Seal to Rotor Groove to a .002 thousand of an inch, metric measurement is .051mm. Sideseal to Rotor Groove .0015 (that's a thousand and a half), metric measurement is .028mm. Sideseal to Cornerseal I use .002 of an inch, metric is .051mm. For Apex Seal to Rotor Housing Width, I like keeping my Apex Seals .0015 to .002 smaller then the Rotor Housing Width.
This will give a tight fit for N/A engines with some really good vacuum. Pulling about 14 to 15 and sometimes 16 inches of vacuum.

2) Turbo and Nitrous engines.
Apex Seal to Rotor Groove to .002 of an inch. Metric is .051mm. Sideseal to Rotor Groove is a bit larger than N/A at .002 instead of .0015. Sideseal to Cornerseal I use .003 thousands of an inch .076mm.
The whole secret here is to make sure you have .003 of an inch on every single Sideseal to Cornerseal gap. The way I do this is very simple. I make sure my .003 or .076mm Feeler Gauge runs smooth back and forth through my gap, but my .004" or metric 102mm Feeler Gauge does not and cannot pass through my .003" gap. This way you're sure to have .003" on every single Sideseal on both rotors and giving you equal compression.
It takes time but the benefits are well worth it. For Apex Seal to Rotor Housing Width I like to stay .0015" to .002" smaller then the Rotor Housing Width. I hope you guys have noticed a slightly bigger gap for Turbo and Nitrous engines, this has brought me some serious reliability and performance.
Just an example I had one engine running 36lbs of boost and a 150 Nitrous Oxide shot all together for 2 hole drag racing seasons and did not take the engine apart. On every single brutal run the engine came back like it was never abused. Fresh and ready for more. I have a lot more success stories, but you guys get my point. 



Boosted and Nitrous Oxide
Naturally Aspirated
Apex Seal to Rotor Groove
0.002" / 0.051mm
Sideseal to Rotor Groove
0.002" / 0.051mm
0.0015" / 0.028mm
Sideseal to Cornerseal
0.003" / 0.076mm
0.002" / 0.051mm
Apex Seal to Rotor Housing Width
0.0015" - 0.002" / 0.028-0.051mm